## Slide 1
Chapter 2
The Physical Layer

## Slide 2: Guided Transmission Media
Guided transmission media
  Persistent storage
  Twisted pairs
  Coaxial cable
  Power lines
  Fiber optics

## Slide 3: Persistent Storage
Consists of magnetic or solid-state storage
Common way to transport data
  Write to persistent storage
  Physically transport the tape or disks to the destination machine
  Read data back again
Cost effective for applications where a high data rate or cost per bit transported is the key factor
Never underestimate the bandwidth of a station wagon full of tapes hurtling down the highway

## Slide 4: Twisted Pairs
A category 5e twisted pair consists of two insulated wires gently twisted together. Four such pairs are typically grouped in a plastic sheath to protect the wires and keep them together.

## Slide 5: Coaxial Cable
A coaxial cable consists of a stiff copper wire as the core, surrounded by an insulating material. The insulator is encased by a cylindrical conductor, often as a closely woven braided mesh. The outer conductor is covered in a protective plastic sheath.

## Slide 6: Power Lines
Using power lines for networking is simple. In this case, a TV and a receiver are plugged into the wall, which must be done anyway because they need power. Then they can send and receive movies over the electrical wiring.

## Slide 7: Fiber Optics (1 of 7)
Allows essentially infinite bandwidth
Must consider costs
  For installation over the last mile and to move bits
Uses
  Long-haul transmission in network backbones
  High-speed LANs
  High-speed Internet access
Key components
  Light source, transmission medium, and detector
Transmission system uses physics

## Slide 8: Fiber Optics (2 of 7)
Figure (a) illustrates a light ray inside a silica fiber impinging on the air/silica boundary at different angles. Figure (b) illustrates light trapped by total internal reflection.

## Slide 9: Fiber Optics (3 of 7)
Transmission of light through fiber
  Attenuation of light through glass
    Dependent on the wavelength of the light
    Defined as the ratio of input to output signal power
Fiber cables
  Similar to coax, except without the braid
Two kinds of signaling light sources
  LEDs (Light Emitting Diodes)
  Semiconductor lasers

## Slide 10: Fiber Optics (4 of 7)
Attenuation of light through fiber in the infrared region is measured in units of decibels (dB) per linear kilometer of fiber.

## Slide 11: Fiber Optics (5 of 7)
Views of a fiber cable

## Slide 12: Fiber Optics (6 of 7)
A comparison of semiconductor diodes and LEDs as light sources.

## Slide 13: Fiber Optics (7 of 7)
Fiber advantages over copper
  Handles higher bandwidth
  Not affected by power surges, electromagnetic interference, power failures, corrosive chemicals
  Thin and lightweight
  Do not leak light
  Difficult to tap
Fiber disadvantage
  Less familiar technology that requires specific engineering skills
  Fibers damaged easily by being bent too much

## Slide 14: Wireless Transmission
The electromagnetic spectrum
  Modulate wave amplitude, frequency, or phase
Frequency hopping spread spectrum
  Transmitter hops from frequency to frequency hundreds of times per second
Direct sequence spread spectrum
  Code sequence spreads data signal over wider frequency band
Ultra-wideband communication
  Communication sends a series of low-energy rapid pulses, varying their carrier frequencies to communicate information

## Slide 15: The Electromagnetic Spectrum
The electromagnetic spectrum and its uses for communication.

## Slide 16: Direct Sequence Spread Spectrum
Direct sequence spread spectrum uses a code sequence to spread the data signal over a wider frequency band.

## Slide 17: Using the Spectrum for Transmission
Radio transmission
  Omnidirectional waves, easy to generate, travel long distances, penetrate buildings
Microwave transmission
  Directional waves requiring repeaters, do not penetrate buildings
Infrared transmission
  Unguided waves used for short-range communication, relatively directional, cheap, easy to build, do not penetrate solid walls
Light transmission
  Unguided optical communication

## Slide 18: Radio Transmission
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth. In the HF band, they bounce off the ionosphere.

## Slide 19: Light Transmission
Convection currents can interfere with laser communication systems. A bidirectional system with two lasers is pictured here.

## Slide 20: From Waveforms to Bits
The theoretical basis for data communication
  Fourier analysis
  Bandwidth-limited signals
The maximum data rate of a channel
Digital modulation
Multiplexing

## Slide 21: Fourier Analysis
We model the behavior of variation of voltage or current with mathematical functions
Fourier series is used
Function reconstructed with

## Slide 22: Bandwidth-Limited Signals (1 of 2)
A binary signal and its root-mean-square Fourier amplitudes. This is followed by successive approximations to the original signal.

## Slide 23: Bandwidth-Limited Signals (2 of 2)
The relation between data rate and harmonics for our example.

## Slide 24: The Maximum Data Rate of a Channel
Nyquist’s theorem
  Maximum data rate = 2Blog2 V bits/sec
Shannon’s formula for capacity of a noisy channel
  Maximum data rate = Blog2 (1 + S/N)bits/sec

## Slide 25: Digital Modulation
Baseband transmission
Bandwidth efficiency
Clock recovery
Balanced signals
Passband transmission

## Slide 26: Baseband Transmission
Line codes: (a) Bits, (b) NRZ, (c) NRZI, (d) Manchester, (e) Bipolar or AMI.

## Slide 27: Bandwidth Efficiency
Bandwidth is often a limited resource
Solution
  Use more than two signaling levels
  By using four voltages we can send 2 bits at once as a single symbol
  Design works as long as the signal at the receiver is sufficiently strong to distinguish the four levels
  Signal rate change is half the bit rate, so the needed bandwidth has been reduced

## Slide 28: Clock Recovery
4B/5B mapping.

## Slide 29: Balanced Signals
Balanced signals
  Signals having as much positive voltage as negative voltage even over short periods of time
  They average to zero (they have no DC electrical component)
Balancing helps to provide transitions for clock recovery
Provides a simple way to calibrate receivers
Straightforward way to construct a balanced code
  Use two voltage levels to represent a logical 1 and a logical zero
  Scheme is called is called bipolar encoding
  Bipolar encoding adds a voltage level to achieve balance

## Slide 30: Passband Transmission (1 of 3)
(a) A binary signal. (b) Amplitude shift keying. (c) Frequency shift keying. (d) Phase shift keying.

## Slide 31: Passband Transmission (2 of 3)
(a) QPSK. (b) QAM-16. (c) QAM-64.

## Slide 32: Passband Transmission (3 of 3)
Gray-coded QAM-16

## Slide 33: Multiplexing
Frequency Division Multiplexing
Time Division Multiplexing
Code Division Multiplexing
Wavelength Division Multiplexing

## Slide 34: Frequency Division Multiplexing (1 of 2)
(a) The original bandwidths. (b) The bandwidths raised in frequency. (c) The multiplexed channel.

## Slide 35: Frequency Division Multiplexing (2 of 2)
Orthogonal frequency division multiplexing (OFDM).

## Slide 36: Time Division Multiplexing
Time Division Multiplexing (TDM)

## Slide 37: Code Division Multiplexing
(a) Chip sequences for four stations. (b) Signals the sequences represent. (c) Six examples of transmissions. (d) Recovery of station C’s signal.

## Slide 38: Wavelength Division Multiplexing
Wavelength division multiplexing

## Slide 39: The Public Switched Telephone Network
Structure of the Telephone System
The Local Loop: Telephone Modems, ADSL, and Fiber
  Telephone modems

## Slide 40: Structure of the Telephone System (1 of 2)
(a) Fully interconnected network. (b) Centralized switch. (c) Two-level hierarchy.

## Slide 41: Structure of the Telephone System (2 of 2)
A typical circuit route for a long-distance call.

## Slide 42: The Local Loop: Telephone Modems, ADSL, and Fiber
Telephone Modems
Digital Subscriber Lines (DSL)
Fiber To The X (FTTX)

## Slide 43: Telephone Modems (1 of 2)
The use of both analog and digital transmission for a computer-to-computer call. Conversion is done by the modems and codecs.

## Slide 44: Telephone Modems (2 of 2)
Some modem standards and their bit rate.

## Slide 45: Digital Subscriber Lines (DSL) (1 of 3)
Bandwidth versus distance over Category 3 UTP for DSL.

## Slide 46: Digital Subscriber Lines (DSL) (2 of 3)
Operation of ADSL using discrete multitone modulation.

## Slide 47: Digital Subscriber Lines (DSL) (3 of 3)
A typical ADSL equipment configuration.

## Slide 48: Fiber To The X (FTTX)
Passive optical network for Fiber To The Home.

## Slide 49: Trunks and Multiplexing
Digitizing Voice Signals
T-Carrier: Multiplexing Digital Signals on the Phone Network
Multiplexing Optical Networks: SONET/SDH

## Slide 50: Digitizing Voice Signals
TDM technique in widespread use today
  Conversion from analog to digital in the end office is needed
  Use a codec to digitize analog signals
  PCM (Pulse Code Modulation) technique used
  Each sample of the amplitude of the signal is quantized to an 8-bit number
  Two versions of quantization are used: μ-law and A-law
  Companding
    Compressing the dynamic range of the signal before it is (evenly) quantized
    Expanding it when the analog signal is recreated
  Analog signal recreated from the quantized samples by playing them out (and smoothing them) over time

## Slide 51: T-Carrier: Multiplexing Digital Signals on the Phone Network (1 of 2)
The T1 carrier (1.544 Mbps).

## Slide 52: T-Carrier: Multiplexing Digital Signals on the Phone Network (2 of 2)
Multiplexing T1 streams into higher carriers.

## Slide 53: Multiplexing Optical Networks: SONET/SDH (1 of 2)
Two back-to-back SONET frames.

## Slide 54: Multiplexing Optical Networks: SONET/SDH (2 of 2)
SONET and SDH multiplex rates.

## Slide 55: Switching
Phone system principal parts
  Outside plant (outside switching offices)
  Inside plant (inside switching offices)
Two different switching techniques
  Circuit switching: traditional telephone system
  Packet switching: voice over IP technology

## Slide 56: Circuit Switching (1 of 2)
(a) Circuit switching. (b) Packet switching.

## Slide 57: Circuit Switching (2 of 2)
Timing of events in (a) circuit switching, (b) packet switching.

## Slide 58: Packet Switching
A comparison of circuit-switched and packet-switched networks.

## Slide 59: Cellular Networks
Mobile phone distinct generations
The initial three generations: 1G, 2G, 3G
  Provided analog voice, digital voice, and both digital voice and data (Internet, email, etc.) respectively
4G technology adds capabilities
  Physical layer transmission techniques and IP-based femtocells
  4G is based on packet switching only (no circuit switching)
5G being rolled out now
  Supports up to 20 Gbps transmissions and denser deployments
  Focus on reducing network latency

## Slide 60: Common Concepts: Cells, Handoff, Paging
(a) Frequencies are not reused in adjacent cells. (b) To add more users, smaller cells can be used.

## Slide 61: First-Generation (1G) Technology: Analog Voice
1946 push to talk systems
1960 IMTS (Improved Mobile Telephone System)
  Two frequencies: one for sending, one for receiving
1983 AMPS (Advanced Mobile Phone System)
  Analog mobile phone system
  Cells are typically 10 to 20 km across
  Used FDM to separate channels
  832 full-duplex channels that consist of a pair of simplex channels used (Frequency Division Duplex)
  Each simplex channel is 30 kHz wide
  832 channels in AMPS are divided into four categories

## Slide 62: Call Management
Outgoing calls
  Phone switched on, number entered, CALL button hit
  Phone transmits called number and its own identity on the access channel
  Base informs the MSC and MSC looks for a channel for the call
Incoming calls
  Idle phones continuously listen to the paging channel to detect messages directed at them
  Packet sent to base station in the current cell as a broadcast on the paging channel
  The called phone responds on the access channel
  Called phone switches to channel and starts ringing sound

## Slide 63: Second-Generation (2G) Technology: Digital Voice
Digital advantages
  Provides capacity gains by allowing voice signals to be digitized and compressed
  Improves security by allowing voice and control signals to be encrypted
  Deters fraud and eavesdropping, whether from intentional scanning or echoes of other calls due to RF propagation
  Enables new services such as text messaging
Three systems developed
  D-AMPS (Digital Advanced Mobile Phone System)
  GSM (Global System for Mobile communications)
  CDMA (Code Division Multiple Access)

## Slide 64: GSM: The Global System for Mobile Communications (1 of 3)
GSM mobile network architecture.

## Slide 65: GSM: The Global System for Mobile Communications (2 of 3)
GSM uses 124 frequency channels, each of which uses an eight-slot TDM system.

## Slide 66: GSM: The Global System for Mobile Communications (3 of 3)
A portion of the GSM framing structure.

## Slide 67: Third-Generation (3G) Technology: Digital Voice and Data
Soft handoff (a) before, (b) during, and (c) after.

## Slide 68: Fourth-Generation (4G) Technology: Packet Switching
Also called IMT Advanced
Based completely on packet-switched technology
EPC (Evolved Packet Core) allows packet switching
  Simplified IP network separating voice traffic from the data network
  Carries both voice and data in IP packets
  Voice over IP (VoIP) network with resources allocated using the statistical multiplexing approaches
  The EPC must manage resources in such a way that voice quality remains high in the face of network resources that are shared among many users

## Slide 69: Fifth-Generation (5G) Technology
Two main factors
  Higher data rates and lower latency than 4G technologies
Technology used to increase network capacity
  Ultra-densification and offloading
  Increased bandwidth with millimeter waves
  Increased spectral efficiency through advances in massive MIMO (Multiple-Input Multiple-Output) technology
Network slicing feature
  Lets cellular carriers create multiple virtual networks on top of the same shared physical infrastructure
  Can devote network portions to specific customer use cases

## Slide 70: Cable Networks
Cable networks
  Will factor heavily into future broadband access networks
Many people nowadays get their television, telephone, and Internet service over cable
2018 DOCSIS standard
  Provides information related to modern cable network architectures

## Slide 71: A History of Cable Networks: Community Antenna Television
An early cable television system.

## Slide 72: Broadband Internet Access Over Cable: HFC Networks (1 of 2)
(a) Hybrid Fiber-Coax cable network. (b) The fixed phone system.

## Slide 73: Broadband Internet Access Over Cable: HFC Networks (2 of 2)
Frequency allocation in a typical cable TV system used for Internet access.

## Slide 74: DOCSIS
DOCSIS (Data Over Cable Service Interface Specification) 3.1 latest version
  Introduced Orthogonal Frequency Division Multiplexing (OFDM)
  Introduced wider channel bandwidth and higher efficiency
  Enabled over 1 Gbps of downstream capacity per home
Extensions to DOCSIS 3.1
  Full Duplex operation (2017) and DOCSIS Low Latency (2018)
Cable Internet subscribers require a DOCSIS cable modem
Modem-to-home network interface: Ethernet connection

## Slide 75: Resource Sharing in DOCSIS Networks: Nodes and Minislots
Typical details of the upstream and downstream channels in North America.

## Slide 76: Communication Satellites
Communication satellites and some of their properties, including altitude above the earth, round-trip delay time, and number of satellites needed for global coverage.

## Slide 77: Geostationary Satellites (1 of 2)
The principal satellite bands.

## Slide 78: Geostationary Satellites (2 of 2)
VSATs using a hub.

## Slide 79: Medium-Earth Orbit Satellites
MEO (Medium-Earth Orbit) satellites
  Found at lower altitudes - between the two Van Allen belts
  Drift slowly in longitude (6 hours to circle the earth)
  Must be tracked as they move through the sky
  Have a smaller footprint on the ground
  Require less powerful transmitters to reach them
Used for navigation systems
Example:
  Constellation of roughly 30 GPS (Global Positioning System) satellites orbiting at about 20,200 km

## Slide 80: Low-Earth Orbit Satellites (1 of 2)
The Iridium satellites form six necklaces around the earth.

## Slide 81: Low-Earth Orbit Satellites (2 of 2)
(a) Relaying in space. (b) Relaying on the ground.

## Slide 82: Terrestrial Access Networks: Cable, Fiber, and ADSL
Similarities
  Comparable service and comparable prices
  Use fiber in the backbone
Differences
  Last-mile access technology at the physical and link layers
  Bandwidth consistency
  Cable subscribers share the capacity of a single node
  Maximum speeds
  Availability
  Security

## Slide 83: Satellites Versus Terrestrial Networks
Communication satellites niche markets
  Rapid deployments
  Places where the terrestrial infrastructure is poorly developed
  When broadcasting is essential
United States has some competing satellite-based Internet providers
Satellite Internet access seeing a growing interest
  In-flight Internet access

## Slide 84: Spectrum Allocation
ISM and U-NII bands used in the United States by wireless devices.

## Slide 85: The Cellular Network
Political and tiny marketing decisions can have a huge impact on the deployment of cellular networks
Areas where U.S. and Europe differ
  Digital mobile phone systems
  Phone numbers
  Widespread use of prepaid mobile phones in Europe
Future areas of concern
  Auctioning of coveted spectrum bands for 5G
  Rise of MVNOs (Mobile Virtual Network Operators)

## Slide 86: The Telephone Network
The relationship of LATAs, LECs, and IXCs. All the circles are LEC switching offices. Each hexagon belongs to the IXC whose number is in it.

## Slide 87: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.